## Slide 1: Chapter 12 Secondary-Storage Structure

## Slide 2: Chapter 12: Secondary-Storage Structure
Overview of Mass Storage Structure
Disk Structure
Disk Attachment
Disk Scheduling
Disk Management
Swap-Space Management
RAID Structure
Stable-Storage Implementation
Tertiary Storage Devices

## Slide 3: Objectives
Describe the physical structure of secondary and tertiary storage devices and the resulting effects on the uses of the devices
Explain the performance characteristics of mass-storage devices
Discuss operating-system services provided for mass storage, including RAID and HSM (Hierarchical Storage Management )

## Slide 4: 12.1 Overview of Mass Storage Structure
Magnetic disks provide bulk of secondary storage of modern computers
  Drives rotate at 60 to 200 times per second
  Transfer rate is rate at which data flow between drive and computer
  Positioning time (random-access time) is time to move disk arm to desired cylinder (seek time) and time for desired sector to rotate under the disk head (rotational latency)
  Head crash results from disk head making contact with the disk surface  That’s bad

## Slide 5: Moving-head Disk Mechanism

## Slide 6: Overview of Mass Storage Structure
Disks can be removable
Drive attached to computer via I/O bus
  Busses vary, including EIDE, ATA, SATA, USB, Fibre Channel (FC), SCSI
  Host controller in computer uses bus to talk to disk controller built into drive or storage array

## Slide 7: Overview of Mass Storage Structure (Cont.)
Magnetic tape
  Was early secondary-storage medium
  Relatively permanent and holds large quantities of data
  Access time slow
  Random access ~1000 times slower than disk
  Mainly used for backup, storage of infrequently-used data, transfer medium between systems
  Kept in spool and wound or rewound past read-write head
  Once data under head, transfer rates comparable to disk
  20-200GB typical storage

## Slide 8: 12.2 Disk Structure
Disk drives are addressed as large 1-dimensional arrays of logical blocks, where the logical block is the smallest unit of transfer.
The 1-dimensional array of logical blocks is mapped into the sectors of the disk sequentially.
  Sector 0 is the first sector of the first track on the outermost cylinder.
  Mapping proceeds in order through that track, then the rest of the tracks in that cylinder, and then through the rest of the cylinders from outermost to innermost.

## Slide 9: 12.3 Disk Attachment
Host-attached storage accessed through I/O ports talking to I/O busses
SCSI itself is a bus, up to 16 devices on one cable, SCSI initiator requests operation and SCSI targets perform tasks
  Each target can have up to 8 logical units (disks attached to device controller)
FC (Fiber Channel) is high-speed serial architecture
  Can be switched fabric with 24-bit address space – the basis of storage area networks (SANs) in which many hosts attach to many storage units
  Can be arbitrated loop (FC-AL) of 126 devices

## Slide 10: Network-Attached Storage (NAS)
Network-attached storage (NAS) is storage made available over a network rather than over a local connection (such as a bus)
NFS and CIFS are common protocols
Implemented via remote procedure calls (RPCs) between host and storage
New iSCSI protocol uses IP network to carry the SCSI protocol

## Slide 11: Storage Area Network (SAN)
Common in large storage environments (and becoming more common)
Multiple hosts attached to multiple storage arrays - flexible

## Slide 12: 12.4 Disk Scheduling
The operating system is responsible for using hardware efficiently — for the disk drives, this means having a fast access time and disk bandwidth.
Access time has two major components
  Seek time is the time for the disk arm to move the heads to the cylinder containing the desired sector.
  Rotational latency is the additional time waiting for the disk to rotate the desired sector to the disk head.
Minimize seek time
Seek time  seek distance
Disk bandwidth is the total number of bytes transferred, divided by the total time between the first request for service and the completion of the last transfer.

## Slide 13: Disk Scheduling (Cont.)
Several algorithms exist to schedule the servicing of disk I/O requests.
We illustrate them with a request queue (0-199 cylinders).
98, 183, 37, 122, 14, 124, 65, 67
Head pointer 53

## Slide 14: FCFS (First Come First Service)
Illustration shows total head movement of 640 cylinders.

## Slide 15: SSTF (Shortest Seek Time First)
Selects the request with the minimum seek time from the current head position.
SSTF scheduling is a form of SJF scheduling; may cause starvation of some requests.
Illustration shows total head movement of 236 cylinders.

## Slide 16: SSTF (Cont.)

## Slide 17: SCAN
The disk arm starts at one end of the disk, and moves toward the other end, servicing requests until it gets to the other end of the disk, where the head movement is reversed and servicing continues.
Sometimes called the elevator algorithm.
Illustration shows total head movement of 208 cylinders.

## Slide 18: SCAN (Cont.)

## Slide 19: C-SCAN
Provides a more uniform wait time than SCAN.
The head moves from one end of the disk to the other. servicing requests as it goes.
When it reaches the other end, however, it immediately returns to the beginning of the disk, without servicing any requests on the return trip.
Treats the cylinders as a circular list that wraps around from the last cylinder to the first one.

## Slide 20: C-SCAN (Cont.)
No service

## Slide 21: C-LOOK (or LOOK)
Versions of SACN and C-SCAN
Arm only goes as far as the last request in each direction, then reverses direction immediately, without first going all the way to the end of the disk.
They look for a request before continuing to move in a given direction.

## Slide 22: C-LOOK (Cont.)

## Slide 23: Selecting a Disk-Scheduling Algorithm
SSTF is common and has a natural appeal
SCAN and C-SCAN perform better for systems that place a heavy load on the disk.
Performance depends on the number and types of requests.
Requests for disk service can be influenced by the file-allocation method.
The disk-scheduling algorithm should be written as a separate module of the operating system, allowing it to be replaced with a different algorithm if necessary.
Either SSTF or LOOK is a reasonable choice for the default algorithm.

## Slide 24: 12.5 Disk Management
Low-level formatting, or physical formatting — Dividing a disk into sectors that the disk controller can read and write.
To use a disk to hold files, the operating system still needs to record its own data structures on the disk.
  Partition the disk into one or more groups of cylinders.
  Logical formatting or “making a file system”.
Boot block initializes system.
  The bootstrap is stored in ROM.
  Bootstrap loader program.
Methods such as sector sparing used to handle bad blocks.

## Slide 25: Booting from a Disk in Windows 2000
The Windows 2000 system places it boot code in the first sector on the hard disk (Master boot record, MBR).
Windows 2000 allows a hard disk to be divided into one or more partitions; one partition, identified as the boot partition, contains the OS ad device drivers.
Once the system identifies the boot partition, it reads the first sector from that partition (which is called the boot sector) and continues with the remainder of the boot process.

## Slide 26: Booting from a Disk in Windows 2000
boot sector

## Slide 27: 12.6 Swap-Space Management
Swap-space — Virtual memory uses disk space as an extension of main memory.
Swap-space can be carved out of the normal file system or, more commonly, it can be in a separate disk partition.
Swap-space management
  4.3BSD allocates swap space when process starts; holds text segment (the program) and data segment.
  Kernel uses swap maps to track swap-space use.
  Solaris 2 allocates swap space only when a page is forced out of physical memory, not when the virtual memory page is first created.

## Slide 28: Swapping on Linux Systems
Linux allows one or more swap areas to be established.
A swap area may be either a swap file on a regular file system or a raw-swap-space partition.
Each swap area consists of a series of 4KB page slots, which are used to hold swapped pages.
Each swap area is associated with a swap map.
  Counter = 0, the corresponding page slot is available.
  Counter >0, the page slot is occupied by a swapped page. The value of the counter indicates the number of mappings to the swapped page. Counter =3, the swapped paged is storing a region of memory shared by three processes.

## Slide 29: Data Structures for Swapping on Linux Systems
4KB
The value of the counter indicates the number of mappings to the swapped page

## Slide 30: 12.7 RAID Structure
RAID (Redundant Arrays of Independent Disks) – multiple disk drives provides reliability via redundancy.
RAID is arranged into seven different levels.
With multiple disks, we can improve the transfer rate by striping data across the disks.
Data striping consists of splitting the bits of each byte across multiple disks – bit level striping
Block-level striping consists of splitting the blocks of each file across multiple disks.

## Slide 31: RAID (cont)
Several improvements in disk-use techniques involve the use of multiple disks working cooperatively.
Disk striping uses a group of disks as one storage unit.
RAID schemes improve performance and improve the reliability of the storage system by storing redundant data.
  Mirroring or shadowing keeps duplicate of each disk.
  Block interleaved parity uses much less redundancy.

## Slide 32: RAID (cont)
RAID level 0: RAID level 0 refers to disk arrays with striping at the level of blocks but without any redundancy.
RAID level 1: RAID level 1 refers to disk mirroring.

## Slide 33: RAID (cont)
RAID level 2: RAID level 2 also known as memory-style error-correcting-code (ECC) organization. The parity bits are used. The disks labeled P store the error-correction bits.

## Slide 34: RAID (cont)
RAID level 3: RAID level 3 refers to bit-interleaved parity organization improves on level 2 by taking into account the fact that, unlike memory systems, disk controllers can detect whether a sector has been read correctly, so a single parity bit can be used for error correction and for detection.

## Slide 35: RAID (cont)
RAID level 4: RAID level 0 refers to block-interleaved parity organization, uses block-level striping, as in RAID 0, and also keeps a parity block on a separate disk for corresponding blocks from N other disks.

## Slide 36: RAID (cont)
RAID level 5: RAID level 5 refers to block-interleaved distributed parity, differs from level 4 by spreading data and parity among all N+1 disks, rather than storing data in N disks and parity in one disk.
  For each block, one of the disks stores the parity, and the others store data.
  With an array of five disks, the parity for the nth block is stored in disk (n mod 5)+1; the nth blocks of the other four disks store actual data for the block.
  A parity block cannot store parity for the blocks in the same disk.

## Slide 37
RAID level 6, P+Q redundancy scheme, is much like RAID 5 but stores extra redundant information to guard against multiple disk failures.
  Instead of parity, error-correcting codes such as Reed-Solomon codes are used. 2 bits of redundant data are stored for every 4 bits of data – compared with 1 parity bit in level 5 – and the system can tolerate two disk failures.
RAID (cont)

## Slide 38: RAID Levels

## Slide 39
RAID 0 provides the performance,
RAID 1 provides the reliability.
RAID 0 +1 : A set of disks are striped, and then the stripe is mirrored to another, equivalent strip
RAID 1+0: Disks are mirrored in pairs and then the resulting mirrored pairs are striped.
RAID 1+0 has some theoretical advantages over RAID 0+1.
For example, if a single disk fails in RAID 0+1, an entire strip is inaccessible, leaving only the other strip available. With a failure in RAID 1+0, a single disk is unavailable, but the disk that mirrors it is still available, as are all the rest of the disks.
RAID (cont)

## Slide 40: RAID (0 + 1) and (1 + 0)

## Slide 41: 12.8 Stable-Storage Implementation
Write-ahead log scheme requires stable storage.
To implement stable storage:
  Replicate information on more than one nonvolatile storage media with independent failure modes.
  Update information in a controlled manner to ensure that we can recover the stable data after any failure during data transfer or recovery.

## Slide 42: 12.9 Tertiary Storage Structure
Low cost is the defining characteristic of tertiary storage.
Generally, tertiary storage is built using removable media
Common examples of removable media are floppy disks and CD-ROMs; other types are available.

## Slide 43: Removable Disks
Floppy disk — thin flexible disk coated with magnetic material, enclosed in a protective plastic case.
  Most floppies hold about 1 MB; similar technology is used for removable disks that hold more than 1 GB.
  Removable magnetic disks can be nearly as fast as hard disks, but they are at a greater risk of damage from exposure.

## Slide 44: Removable Disks (Cont.)
A magneto-optic disk records data on a rigid platter coated with magnetic material.
  Laser heat is used to amplify a large, weak magnetic field to record a bit.
  Laser light is also used to read data (Kerr effect).
  The magneto-optic head flies much farther from the disk surface than a magnetic disk head, and the magnetic material is covered with a protective layer of plastic or glass; resistant to head crashes.
Optical disks do not use magnetism; they employ special materials that are altered by laser light.

## Slide 45: WORM Disks
The data on read-write disks can be modified over and over.
WORM (“Write Once, Read Many Times”) disks can be written only once.
Thin aluminum film sandwiched between two glass or plastic platters.
To write a bit, the drive uses a laser light to burn a small hole through the aluminum; information can be destroyed by not altered.
Very durable and reliable.
Read Only disks, such as CD-ROM and DVD, come from the factory with the data pre-recorded.

## Slide 46: Tapes
Compared to a disk, a tape is less expensive and holds more data, but random access is much slower.
Tape is an economical medium for purposes that do not require fast random access, e.g., backup copies of disk data, holding huge volumes of data.
Large tape installations typically use robotic tape changers that move tapes between tape drives and storage slots in a tape library.
  stacker – library that holds a few tapes
  silo – library that holds thousands of tapes
A disk-resident file can be archived to tape for low cost storage; the computer can stage it back into disk storage for active use.

## Slide 47: Operating System Support
Major OS jobs are to manage physical devices and to present a virtual machine abstraction to applications
For hard disks, the OS provides two abstraction:
  Raw device – an array of data blocks.
  File system – the OS queues and schedules the interleaved requests from several applications.

## Slide 48: Application Interface
Most OSs handle removable disks almost exactly like fixed disks — a new cartridge is formatted and an empty file system is generated on the disk.
Tapes are presented as a raw storage medium, i.e., and application does not open a file on the tape, it opens the whole tape drive as a raw device.
Usually the tape drive is reserved for the exclusive use of that application.
Since the OS does not provide file system services, the application must decide how to use the array of blocks.
Since every application makes up its own rules for how to organize a tape, a tape full of data can generally only be used by the program that created it.

## Slide 49: Tape Drives
The basic operations for a tape drive differ from those of a disk drive.
locate positions the tape to a specific logical block, not an entire track (corresponds to seek).
The read position operation returns the logical block number where the tape head is.
The space operation enables relative motion.
Tape drives are “append-only” devices; updating a block in the middle of the tape also effectively erases everything beyond that block.
An EOT mark is placed after a block that is written.

## Slide 50: File Naming
The issue of naming files on removable media is especially difficult when we want to write data on a removable cartridge on one computer, and then use the cartridge in another computer.
Contemporary OSs generally leave the name space problem unsolved for removable media, and depend on applications and users to figure out how to access and interpret the data.
Some kinds of removable media (e.g., CDs) are so well standardized that all computers use them the same way.

## Slide 51: Hierarchical Storage Management (HSM)
A hierarchical storage system extends the storage hierarchy beyond primary memory and secondary storage to incorporate tertiary storage — usually implemented as a jukebox of tapes or removable disks.
Usually incorporate tertiary storage by extending the file system.
  Small and frequently used files remain on disk.
  Large, old, inactive files are archived to the jukebox.
HSM is usually found in supercomputing centers and other large installations that have enormous volumes of data.

## Slide 52: Speed
Two aspects of speed in tertiary storage are bandwidth and latency.
Bandwidth is measured in bytes per second.
  Sustained bandwidth – average data rate during a large transfer; # of bytes/transfer time. Data rate when the data stream is actually flowing.
  Effective bandwidth – average over the entire I/O time, including seek or locate, and cartridge switching. Drive’s overall data rate.

## Slide 53: Speed (Cont.)
Access latency – amount of time needed to locate data.
  Access time for a disk – move the arm to the selected cylinder and wait for the rotational latency; < 35 milliseconds.
  Access on tape requires winding the tape reels until the selected block reaches the tape head; tens or hundreds of seconds.
  Generally say that random access within a tape cartridge is about a thousand times slower than random access on disk.
The low cost of tertiary storage is a result of having many cheap cartridges share a few expensive drives.
A removable library is best devoted to the storage of infrequently used data, because the library can only satisfy a relatively small number of I/O requests per hour.

## Slide 54: Reliability
A fixed disk drive is likely to be more reliable than a removable disk or tape drive.
An optical cartridge is likely to be more reliable than a magnetic disk or tape.
A head crash in a fixed hard disk generally destroys the data, whereas the failure of a tape drive or optical disk drive often leaves the data cartridge unharmed.

## Slide 55: Cost
Main memory is much more expensive than disk storage
The cost per megabyte of hard disk storage is competitive with magnetic tape if only one tape is used per drive.
The cheapest tape drives and the cheapest disk drives have had about the same storage capacity over the years.
Tertiary storage gives a cost savings only when the number of cartridges is considerably larger than the number of drives.

## Slide 56: Price per Megabyte of DRAM From 1981 to 2008

## Slide 57: Price per Megabyte of Magnetic Hard Disk From 1981 to 2008

## Slide 58: Price per Megabyte of a Tape Drive From 1984-2008

## Slide 59: End of Chapter 12